## Slide 1: Hardware Trojan Detection with Symbolic QED and Symbolic Initial States
1
Trojan Characteristics
  Exist in pre-silicon design.
  Cause wrong logic value(s).
Effective and Quick Detection
  100% of injected Trojans in RISC-V cores detected.
  Avg. runtime: 11 seconds
  Traces: 5-6 clock cycles
No False Positives
Time
Billions of cycles delay.
Trojan undetected.
Trojan
Activates
5-6
cycles
Reset State
Symbolic State
1-2
cycles
Trojan Detected
Debug

## Slide 2: How does it work?
Symbolic QED with Symbolic Initialization
  Interleave original and duplicate instructions.
  Check equality of original/duplicate registers.
  Constrain initial state to avoid false positives:
    “In-flight” instructions commit before test.
    In QED-Consistent state before test.
    Operand data available during test.
  BMC: returns shortest counterexample.
2

## Slide 3: What experiments did we do?
Trojan Insertion in RISC-V Cores
  Variety of Trojan Activation Criteria
    Large counter reaches specific value.
    Subset of wires reaches specific value.
    Specific sequence of values on a wire.
    Event counter reaches specific value.
3

## Slide 4: What experiments did we do? (2)
  Variety of Trojan Effects
    Any instruction changed to NOP.
    Opcode of an instruction changed.
    Next register read corrupted.
    Next result of execution stage changed.
    Commit before operand data available.
  All pairs of (Trojan Activation, Effect) tested
4