## Slide 1: Symbolic QED Pre-silicon Verification for Automotive Microcontroller Cores: Infineon Case Study
K Devarajegowda, S Simon,
R Schnieder, W Ecker
M Fadiheh, D Stoffel, W Kunz
E Singh, K Ganesan,
C Barrett, S Mitra

## Slide 2: Results: Infineon Case Study
16
Designs
Microcontroller cores, automotive products
Extensively verified (simulation, formal)
Logic Bugs
Symbolic QED detected ALL (known) bugs & more (specification errors)
Effort
8x - 60x improved (less) verification effort

## Slide 3: Must Rethink Pre-Silicon Verification
Very few “real” innovations over past decade
  Race against time & complexity
Product features limited by verification
  Existing techniques not sustainable

## Slide 4: Infineon Study: Evaluate Symbolic QED
Stanford results [Lin ITC 15, Singh IEEE TCAD 18]
  Highly effective for logic bugs
  Runtime few minutes to few hours
  No design-specific properties
  Billion transistor-scale designs
  Processor cores, uncore, accelerators

## Slide 5: Case Study Objectives
Robust Industrial Flow
Directed Tests, Constrained Random Tests, Infineon Formal
Symbolic QED
  Characterize bugs detected
  Quantify manual effort
  Quantify runtime

## Slide 6: Designs Analyzed
Custom microcontroller core (16 versions, verified over 5 years)
3D
camera
Airbag
Pressure
Monitor
And
more…

## Slide 7: Automotive Microcontroller Core
60 instructions, 1.8K flip-flops, 70K gates
    ASIL rated
    Numerous corner case simulation scenarios
16 versions over 5 years
    Feature updates & architecture upgrades
    Bug fixes
ASIL: Automotive Safety Integrity Level

## Slide 8: Infineon Verification Flow
Robust Infineon approach: proven record
Microcontroller extensively verified over 5 years
    Directed Simulation Tests (DST)
    Infineon Formal (IF)
    Constrained Random Simulation (CRS)
CRS
IF
DST

## Slide 9: Traditional Bounded Model Checking
Design
Property
BMC Tool
Bug found
Chart: 
| Category 1
Series 1 | 2
Series 2 | 16
ISA
Properties
Manual
Effort
Challenges:
1. Doesn’t scale (large designs)
2. Significant manual effort
Bound = k
∃(program of length ≤ k)
Property violated?

## Slide 10: Symbolic QED
Design
BMC Tool
Bug found
∃QED program of length ≤ k that fails?
Bound = k
Chart: 
| Category 1
Series 1 | 2
Series 2 | 16
Manual
Effort
1. Compositional:
  Scalable to large designs
2. Much lower manual effort
ISA +
QED Module

## Slide 11: What is a QED program?
Many QED techniques: EDDI-V, PLC, CFCSS-V, CFTSS-V
Example: EDDI-V
Duplicate Instructions
Original Instructions
R1 == R17
R2 == R18
Check:
R17 ← R1;R18 ← R2;
R17 ← R17 + 5
R18 ← R18 * R17
R1 ← R1 + 5
R2 ← R2 * R1
R2 ← R1
R18 ← R17
R17 ← R1;R18 ← R2;
Interleaving 1
R17 ← R1;R18 ← R2;
Interleaving 3…
R17 ← R1;R18 ← R2;
Interleaving 2
R1 == R17
R2 == R18
Check:
R1 == R17
R2 == R18
Check:
R1 == R17
R2 == R18
Check:
R2 ← R1
R17 ← R17 + 5
R17 ← R17 + 5
R18 ← R18 * R17
R18 ← R18 * R17
R18 ← R18 * R17
R1 ← R1 + 5
R1 ← R1 + 5
R1 ← R1 + 5
R17 ← R17 + 5
R2 ← R2 * R1
R18 ← R17
R18 ← R17
R18 ← R17
R2 ← R2 * R1
R2 ← R2 * R1
R2 ← R1
R2 ← R1
QED module ensures all possible interleavings analyzed
Plus
more

## Slide 12: 1.Characterize Bugs Detected
0%
+7%
Symbolic QED detected ALL (known) bugs
And more (specification errors: +7%)
Infineon Verification flow
Symbolic QED
100%

## Slide 13: 2.Quantify Effort: Reused Designs
Chart: 
| Re-used designs
Infineon Flow | 120
Symbolic QED | 2
6
Person
months
2
Person
days
Most Infineon designs are reused
    Feature updates
    Architecture upgrades
Symbolic QED: 60X improvement
Infineon
Flow
Symbolic QED

## Slide 14: 2.Quantify Effort: Designs from Scratch
  Rarely designs from scratch
Symbolic QED: 8X improvement
17
Person
months
Chart: 
| Re-used designs
Infineon Flow | 17
Symbolic QED | 2
17
Person
months
2
Person
months
Infineon
Flow
Symbolic QED

## Slide 15: 3.Quantify Runtime
Short error trace length (4-10 instructions)
Significant benefits: bug localization and debug
Short runtime (6-12 seconds)
 | Error Trace Length [min, avg, max] | Bug Detection Runtime [min, avg, max]
Symbolic QED | [4, 6, 10] instructions | [6, 8, 12] seconds

## Slide 16: Bigger Designs?
OpenSPARC T2 SoC case study [Lin ITC 15, Singh IEEE TCAD 18]
    0.5 Billion transistors
    Difficult industry logic bugs
    Runtime: 20 min. to 7 hrs.
Bigger Infineon designs: ongoing study
    Phase-1 implementation completed

## Slide 17: Conclusion
Symbolic QED
All (known) logic bugs & more detected
Product Impact
Shorter Time-to-Market
Ongoing
Infineon Symbolic QED efforts
60x verification productivity improvement
New design features
Symbolic QED beyond design verification

## Slide 18: Acknowledgements
Stanford acknowledges:
  DARPA
  Stanford SystemX alliance

## Slide 19
Thank You!

## Slide 20: Conclusion
Symbolic QED
All (known) logic bugs & more detected
Product Impact
Shorter Time-to-Market
Ongoing
Infineon Symbolic QED efforts
60x verification productivity improvement
New design features
Symbolic QED beyond design verification