## Slide 1
Hardware Trojan Detection with Symbolic QED: Symbolic Initial States
1-Department of EE, 2-Department of CS,
Stanford University
Shashank Nuthakki1, Karthik Ganesan1, Mohammad Rahmani Fadiheh3,
Eshan Singh1, Dominik Stoffel3, Wolfgang Kunz3,
Clark Barrett2, Subhasish Mitra1,2
3-Department of ECE,
Technische Universität Kaiserslautern, Germany
Notes: 0

## Slide 2: Problem: Hardware Trojans
Definition [Hardware Trojan]
  Malicious part of design unknown to designer.
Scope for this talk
  Processor cores only.
  Trojan exists in pre-silicon design (i.e., RTL).
  Trojan causes incorrect logic value(s).
  Goal: detect the Trojan (not fix it).
Notes: Explain what a hardware Trojan is, and explain that in this talk we are only talking about Trojans which cause incorrect logic value(s), and exist in pre-silicon design.
Also our goal is to simply detect the Trojan (not fix it).

## Slide 3: Why Is This Problem Difficult?
Hardware Trojan example
  Attacker inserts 128-bit counter in processor core.
  Opcode forced to NOP when counter=2127.
All existing pre-silicon verification methods fail
  Don’t know Trojan design a priori.
  Simulation: Which program to run? Also too slow.
  Conventional Formal: Which property to check?
Notes: Why is this problem difficult to solve?
First we give an example of a hardware Trojan that causes incorrect values in a processor core. There is a long counter, in the design that requires 2^127 clock cycles to activate an attack. The opcode of the current instruction is changed to ‘NOP’ when the Trojan activates.

## Slide 4: Symbolic QED: A New Method
3
Pre-silicon formal analysis. Derived from testing ideas.
Demonstrated on industrial and open-source cores.
Previously unknown “difficult” logic bugs found (confirmed & fixed by designers)
Few minutes per run
Automatic: no manual properties 10× productivity improvement expected
[Lin ITC 15, Fadiheh DATE 18, Singh IEEE TCAD 18]

## Slide 5: SQED Concept: QED Tests
4
void matgen (REAL a[], int lda, int n, REAL b[], REAL *norma)
{
int init, i, j;
init = 1325;
*norma = 0.0;
for (j = 0; j < n; j++) {
for (i = 0; i < n; i++) {
init = 3125*init % 0x100000000l;
a[lda*j+i] = (init - 32768.0)/16384.0;
*norma = (a[lda*j+i] > *norma) ? a[lda*j+i] : *norma;
}
}
for (i = 0; i < n; i++) {
b[i] = 0.0;
}
for (j = 0; j < n; j++) {
for (i = 0; i < n; i++) {
b[i] = b[i] + a[lda*j+i];
}
}
return;
}
void dgefa(REAL a[], int lda, int n, int ipvt[], int *info){
/* internal variables */
REAL t;
int j,k,kp1,l,nm1;
/* gaussian elimination with partial pivoting */
*info = 0;
nm1 = n - 1;
if (nm1 >= 0) {
for (k = 0; k < nm1; k++) {
kp1 = k + 1;
/* find l = pivot index */
l = idamax(n-k,&a[lda*k+k],1) + k;
ipvt[k] = l;
/* zero pivot implies this column already
triangularized */
if (a[lda*k+l] != ZERO) {
/* interchange if necessary */
if (l != k) {
t = a[lda*k+l];
a[lda*k+l] = a[lda*k+k];
a[lda*k+k] = t;
}
/* compute multipliers */
t = -ONE/a[lda*k+k];
dscal(n-(k+1),t,&a[lda*k+k+1],1);
/* row elimination with column indexing */
for (j = kp1; j < n; j++) {
t = a[lda*j+l];
if (l != k) {
a[lda*j+l] = a[lda*j+k];
a[lda*j+k] = t;
}
daxpy(n-(k+1),t,&a[lda*k+k+1],1,
&a[lda*j+k+1],1);
}
}
else {
*info = k;
}
}
}
ipvt[n-1] = n-1;
if (a[lda*(n-1)+(n-1)] == ZERO) *info = n-1;
checkExpected(a, ipvt, info);
return;
}
void dgesl(REAL a[],int lda,int n,int ipvt[],REAL b[],int job )
{
REAL t;
int k,kb,l,nm1;
nm1 = n - 1;
if (job == 0) {
/* job = 0 , solve a * x = b
first solve l*y = b */
if (nm1 >= 1) {
for (k = 0; k < nm1; k++) {
l = ipvt[k];
t = b[l];
if (l != k){
b[l] = b[k];
b[k] = t;
}
daxpy(n-(k+1),t,&a[lda*k+k+1],1,&b[k+1],1 );
}
}
/* now solve u*x = y */
for (kb = 0; kb < n; kb++) {
k = n - (kb + 1);
b[k] = b[k]/a[lda*k+k];
t = -b[k];
daxpy(k,t,&a[lda*k+0],1,&b[0],1 );
}
}
else {
QED Trace
Validation program
Check end_result
R17 ← R17 + 5
R18 ← R18 – R17
R19 ← R17 * R18
R1 ← R1 + 5
R2 ← R2 – R1
R3 ← R1 * R2
R1 == R17
R2 == R18
R3 == R19
R17 ← R1; R18 ← R2; R19 ← R3
Quick!
Notes: First, need to explain what QED tests are and what the EDDI-V transformation does.
4

## Slide 6: SQED Concept: Formal Analysis
5
Formal Tool
Counter-example = bug trace (failing program)
If any QED check violated
“Universal” Property +
QED-consistent initial state
Design + QED Module
(no hardware overhead)
[Lin ITC 15, Singh IEEE TCAD 18]

## Slide 7: SQED Concept: Formal Analysis (2)
Exhaustiveness of formal approach
  SQED searches over all such programs.
  Tries 2 instruction programs first. Then 4,6,…
  Returns the shortest failing program (if exists).
Notes: As you can see, formal is what enables the exhaustiveness of the approach.

## Slide 8: SQED Has Trouble With Trojans
SQED will detect Trojan, given long-enough time.
Tools handle 30 cycles for large cores.
Issue: Trojan wont activate starting from reset!
Counter=0
Counter=1
Counter=
2127-30
Start
Counter=
2127
(Need to start here)
(Trojan activates!)
Notes: Why does SQED have trouble finding such a Trojan?
As you recall, the tool gradually unrolls the circuit one clock cycle at a time and searches for a counterexample at each unrolling.
From our experiments, we have observed that BMC typically runs up to around 30 cycles for large processor cores. If starting from reset, this is clearly not enough for the Trojan to activate, so the tool will end up not considering any states where the Trojan could activate. In other words, the EDDI-V test shown on the previous slide wouldn’t even be considered.
But as we explained, we could also start the formal analysis from a starting state that is not a reset state. How about that? Clearly, we need to start in a state that is within 30 cycles of the Trojan activation. The problem is the Trojan design is not known a priori – we would not know how long the simulation is supposed to run for to get to such a “close state”, and we cannot even verify if a state is close to that.

## Slide 9: Symbolic Initial States: Possible Fix
Formal tool can represent initial state symbolically.
Analyze all combinations of initial state and instructions.
Includes initial states “close” to Trojan activation.
Notes: Therefore, we want to be able to relax the assumption of starting in a concrete QED-consistent state, and allow the input state as well to be chosen by the formal tool. For example, ideally, we would like to start formal analysis right before the Trojan activates, so BMC will be effective again.

## Slide 10: How To Catch Trojan Example
Initialization: R1 = R17 = 0;
Counter = 2127-2
R1 ← R1 + 2
Counter = 2127-1
Notes: Here is an example showing how symbolic initialization could help to catch the Trojan. Assume we could start in a state with all the registers holding zero values, but the counter value is right before the trojan is going to go off. Then, the following EDDI-V test will catch the Trojan.

## Slide 11: How To Catch Trojan Example
Initialization: R1 = R17 = 0;
Counter = 2127-2
Counter = 2127
R1 ← R1 + 2
Counter = 2127-1
R17 ← R17 + 2
Notes: Here is an example showing how symbolic initialization could help to catch the Trojan. Assume we could start in a state with all the registers holding zero values, but the counter value is right before the trojan is going to go off. Then, the following EDDI-V test will catch the Trojan.

## Slide 12: How To Catch Trojan Example
Initialization: R1 = R17 = 0;
Counter = 2127-2
Counter = 2127
Check R1 == R17 (Fails!)
R1 ← R1 + 2
Counter = 2127-1
Trojan Detected.
(Trojan activates!)
NOP
Notes: Here is an example showing how symbolic initialization could help to catch the Trojan. Assume we could start in a state with all the registers holding zero values, but the counter value is right before the trojan is going to go off. Then, the following EDDI-V test will catch the Trojan.

## Slide 13: Challenge : Avoiding False Positives
Cannot use unconstrained initialization: false positives
  Unconstrained initial state may not be QED-consistent.
  Unconstrained initial state may not be reachable.
Constrain tool to only consider reachable states?
  Not feasible – requires solving for reachable set.
  Problem has been unsolved for decades…
Notes: Now, in an unconstrained setup, the initial state is no longer required QED-consistent, and the initial state is no longer required to be reachable. The problem is that we may get false positives if the design is such that the ISA is not necessarily valid when we don’t start from a state reachable from a reset state.
Isn’t it simple to just constrain the tool to only reachable states? Not at all…

## Slide 14: False Positive Example (No Trojan)
R1 ← R1 + 2
R9←R1; R10←R2; R11←R3; …
0x00
R0
0x00
R1
0x00
R2
0x00
R3
0x00
R4
0x00
R5
0x00
R6
0x00
R7
0x00
R8
0x0A
R9
0x00
R10
0x00
R11
0x00
R12
0x00
R13
0x00
R14
0x00
R15
Original
Duplicate
Register File (initialization):
Notes: Here is an example showing how a false positive can happen – lets say we started the test in a state where the registers are not QED consistent. Then we will fail multiple checks, even with no Trojan.

## Slide 15: False Positive Example (No Trojan)
R9 ← R9 + 2
R1 ← R1 + 2
R9←R1; R10←R2; R11←R3; …
0x00
R0
0x00
R1
0x00
R2
0x00
R3
0x00
R4
0x00
R5
0x00
R6
0x00
R7
0x00
R8
0x0A
R9
0x00
R10
0x00
R11
0x00
R12
0x00
R13
0x00
R14
0x00
R15
Original
Duplicate
0x00
R0
0x02
R1
0x00
R2
0x00
R3
0x00
R4
0x00
R5
0x00
R6
0x00
R7
0x00
R8
0x0A
R9
0x00
R10
0x00
R11
0x00
R12
0x00
R13
0x00
R14
0x00
R15
Register File (state):
Notes: Here is an example showing how a false positive can happen – lets say we started the test in a state where the registers are not QED consistent. Then we will fail multiple checks, even with no Trojan.

## Slide 16: False Positive Example (No Trojan)
R9 ← R9 + 2
R10 ← R9 + 6
R1 ← R1 + 2
R9←R1; R10←R2; R11←R3; …
0x00
R0
0x00
R1
0x00
R2
0x00
R3
0x00
R4
0x00
R5
0x00
R6
0x00
R7
0x00
R8
0x0A
R9
0x00
R10
0x00
R11
0x00
R12
0x00
R13
0x00
R14
0x00
R15
Original
Duplicate
0x00
R0
0x02
R1
0x00
R2
0x00
R3
0x00
R4
0x00
R5
0x00
R6
0x00
R7
0x00
R8
0x0A
R9
0x00
R10
0x00
R11
0x00
R12
0x00
R13
0x00
R14
0x00
R15
0x00
R0
0x02
R1
0x00
R2
0x00
R3
0x00
R4
0x00
R5
0x00
R6
0x00
R7
0x00
R8
0x0C
R9
0x00
R10
0x00
R11
0x00
R12
0x00
R13
0x00
R14
0x00
R15
Register File (state):
Notes: Here is an example showing how a false positive can happen – lets say we started the test in a state where the registers are not QED consistent. Then we will fail multiple checks, even with no Trojan.

## Slide 17: False Positive Example (No Trojan)
R9 ← R9 + 2
R10 ← R9 + 6
R2 ← R1 + 6
R1 ← R1 + 2
R9←R1; R10←R2; R11←R3; …
0x00
R0
0x00
R1
0x00
R2
0x00
R3
0x00
R4
0x00
R5
0x00
R6
0x00
R7
0x00
R8
0x0A
R9
0x00
R10
0x00
R11
0x00
R12
0x00
R13
0x00
R14
0x00
R15
Original
Duplicate
0x00
R0
0x02
R1
0x00
R2
0x00
R3
0x00
R4
0x00
R5
0x00
R6
0x00
R7
0x00
R8
0x0A
R9
0x00
R10
0x00
R11
0x00
R12
0x00
R13
0x00
R14
0x00
R15
0x00
R0
0x02
R1
0x00
R2
0x00
R3
0x00
R4
0x00
R5
0x00
R6
0x00
R7
0x00
R8
0x0C
R9
0x00
R10
0x00
R11
0x00
R12
0x00
R13
0x00
R14
0x00
R15
0x00
R0
0x02
R1
0x00
R2
0x00
R3
0x00
R4
0x00
R5
0x00
R6
0x00
R7
0x00
R8
0x0C
R9
0x12
R10
0x00
R11
0x00
R12
0x00
R13
0x00
R14
0x00
R15
Register File (state):
Notes: Here is an example showing how a false positive can happen – lets say we started the test in a state where the registers are not QED consistent. Then we will fail multiple checks, even with no Trojan.

## Slide 18: False Positive Example (No Trojan)
R9 ← R9 + 2
R10 ← R9 + 6
R2 ← R1 + 6
Check R1 == R9 (Fails!)
Check R2 == R10 (Fails!)
R1 ← R1 + 2
False Positive – No Trojan in Design.
R9←R1; R10←R2; R11←R3; …
0x00
R0
0x00
R1
0x00
R2
0x00
R3
0x00
R4
0x00
R5
0x00
R6
0x00
R7
0x00
R8
0x0A
R9
0x00
R10
0x00
R11
0x00
R12
0x00
R13
0x00
R14
0x00
R15
Original
Duplicate
0x00
R0
0x02
R1
0x00
R2
0x00
R3
0x00
R4
0x00
R5
0x00
R6
0x00
R7
0x00
R8
0x0A
R9
0x00
R10
0x00
R11
0x00
R12
0x00
R13
0x00
R14
0x00
R15
0x00
R0
0x02
R1
0x00
R2
0x00
R3
0x00
R4
0x00
R5
0x00
R6
0x00
R7
0x00
R8
0x0C
R9
0x00
R10
0x00
R11
0x00
R12
0x00
R13
0x00
R14
0x00
R15
0x00
R0
0x02
R1
0x00
R2
0x00
R3
0x00
R4
0x00
R5
0x00
R6
0x00
R7
0x00
R8
0x0C
R9
0x12
R10
0x00
R11
0x00
R12
0x00
R13
0x00
R14
0x00
R15
0x00
R0
0x02
R1
0x08
R2
0x00
R3
0x00
R4
0x00
R5
0x00
R6
0x00
R7
0x00
R8
0x0C
R9
0x12
R10
0x00
R11
0x00
R12
0x00
R13
0x00
R14
0x00
R15
Register File (state):
Notes: Here is an example showing how a false positive can happen – lets say we started the test in a state where the registers are not QED consistent. Then we will fail multiple checks, even with no Trojan.

## Slide 19: Avoiding False Positives: Two Steps
Defining “bug-free” operation of a core
  Two basic assumptions (any core should satisfy).
Defining QED-constraints
  Three constraints on starting state.
  Enforced by formal tool.
Observation: QED test fail means assumption(s) violated.
Notes: Therefore, we require some constraints on the starting state and a definition of what is ”correct behavior” of the processor core.
In experiments, we are able to observe the following.

## Slide 20: What experiments did we do?
Trojan Insertion in open-source RISC-V cores
3000 experiments. All scenarios (>95 papers surveyed).
Scenario | Num. Experiments (in-order) | Num. Experiments (superscalar) | Coverage | False Positives | Avg. Runtime (in-order) | Avg. Runtime (ss)
Counter, changes opcode | 8 | 8 | 100% | None | 11 sec. | 20 min.
Counter, corrupts read | 8 | 8 | 100% | None |  | 
Counter, corrupts execution | 8 | 8 | 100% | None |  | 
Internal wires, changes opcode | 64 | 64 | 100% | None |  | 
Internal wires, corrupts read | 64 | 64 | 100% | None |  | 
Internal wires, corrupts execution | 800 | 1800 | 100% | None |  | 
Sequence, changes opcode | 24 | 32 | 100% | None |  | 
Sequence, corrupts read | 24 | 32 | 100% | None |  | 
Sequence, corrupts execution | 24 | 32 | 100% | None |  | 
Counter, corrupts ROB | N/A | 8 | 100% | None |  | 
Internal wires, corrupts ROB | N/A | 8 | 100% | None |  | 
Sequence, corrupts ROB | N/A | 32 | 100% | None |  | 
Notes: Now – to get into details of what experiments we did.. We inserted a wide variety of Trojans into RISC-V cores.

## Slide 21: Results Summary (1)
100% injected Trojans in RISC-V cores detected.
No false positives.
Notes: First – we detected all of these Trojans, with no false positives.

## Slide 22: Results Summary (2)
In-order core (V-Scale):
  Corresponds to 5-6 clock cycles.
  Average runtime of 11 seconds.
Superscalar core (RIDECORE):
  Corresponds to 8 clock cycles.
  Average runtime of 20 minutes.
Notes: And here are more details about the bug trace lengths produced as well as the runtime required for finding these Trojans.

## Slide 23: Future Work
Extension to stand-alone accelerators.
Incorporate other QED transformations.
Notes: Future Work

## Slide 24: Backup Slides
Notes: Backup Slides Follow

## Slide 25: “Bug-Free” Cores: Assumption 1
Equal result for same operation, same data
  I1, I2 : two instructions with same opcode.
  If operands equal, I1, I2 commit same value.
Example
  Rd1 = 1 + 2; Rd2 = 1 + 2;
  Same values written, regardless of Rd1, Rd2.
  Also, context within program has no impact.
Notes: The first assumption states that if we have the same operation on the same data, it writes the same result to state. Also the context within program has no impact.
An example is shown here. Importantly – we do not say assume anything about Rd1 and Rd2 having value ‘3’. We just require that the value written is consistent between the two computations.

## Slide 26: “Bug-Free” Cores: Assumption 2
Consistent data across dependent instructions
  I1, I2. Assume I2 RAW dependent on I1.
  Assume I1 last dependency for operand s.
  Then I2 uses value computed by I1 for s.
Example (a two instruction program)
  I1: R1 = 5; I2 : R2 = R1 + 3.
  Then I2 uses value ‘5’ for R1.
Notes: Second assumption states that anytime we have a dependency, the latestt data is forwarded to be used in the dependent instruction.
An example is shown here.

## Slide 27: QED-Constraints on Starting State (1)
“Symbolic In-flight (SIF) instructions”
  Unfinished instruction bits populated by tool.
Constraint 1 (unfinished instructions finish eventually)
  time when SIF instructions commit.
Constraint 2 (QED-consistent start for analysis)
  At architectural state QED-consistent.
  (Formal analysis begins at ).
Notes: Now lets talk about constraints on starting state.
We define symbolic in flight instructions to mean unfinished instructions. These exist because the design initializes the state of the system, and therefore it populates the state bits throughout the pipeline (which would normally include the state bits for instructions that are still passing through the pipeline).
Then constraint 1 says there exists a finite time by which SIF instructions done.
Then constraint 2 states that also the architectural state is QED-consistent at that time.

## Slide 28: QED-Constraints on Starting State (2)
Constraint 3 (Data availability during formal analysis)
  If data available at , same data is used.
  If not, waiting on earlier SQED instruction.
Example
  At let R1=5.
  SQED Instructions: R2=R1+2; R3=R2+1.
  ‘5’ is used for R1.
  R3 waits for resulting R2.
Notes: Constraint 3 simply states that if the operand data of any instruction was available at TC, it matches what is stored in the architectural state then. If not, it is waiting on an earlier instruction.

## Slide 29: Illustration of QED-Constraints
Fetch
Time
MOV R1, #2
Initialization
(SIF Insts)
Dispatch/EX
Commit
Cycle 1
Cycle 2
Pipeline stages
Cycle 3 ()
State
Cycle 4
NOP
R1 = 3, R9 = 2
R1 = 2, R9 = 2
R1=R1+5
NOP
NOP
NOP
R1 = 2, R9 = 2
NOP
R1=2+5
R1=7
R1 = 2, R9 = 2
R9=2+5
R1=R1-2
R1 = 7, R9 = 2
R1=7-2
…
R9=R9+5
R1=5
R9=R9-2
Notes: Here is an illustration of the QED-constraints for an in-order three-stage pipeline.
The initialization – happens first. All SIF instructions that are flowing through the pipeline are shown in yellow. The state is shown on the right.
The starting state is not QED- consistent, but after the first SIF instruction commits it is. Afterwards, the first SQED instruction is fetched..
After two cycles, we reach TC (all the orange stuff – SIF stuff is out of the pipeline. Then, the first SQED instruction commits, and the duplicates follow.

## Slide 30: What experiments did we do? (1)
Trojan Activation Criteria
  X1 bit counter reaches a specific value.
  M2 internal wires reach a specific state.
  N consecutive bit-patterns on M1 internal wires.
  An above event happens X2 times.
Wide range tested for X1, X2, M1, M2, N.
Notes: Here are the details on activation criteria.

## Slide 31: What experiments did we do? (2)
Trojan Effects
  Opcode of in-flight instruction changed.
  Next register read corrupted.
  Next execution unit result changed.
  Reorder-buffer entries corrupted to commit next inst.
Notes: Here are the details on trojan effects.

## Slide 32: How many experiments did we do?
Total number of Trojan scenarios (parameter combinations):
  156 types for in-order cores (no reorder-buffer).
  195 types for out-of-order cores.
Total number of Trojan experiments ran:
  >1000 for in-order cores.
  1995 for out-of-order core (RIDECORE).
Notes: Here are the details on trojan effects.